## Slide 1: Bayesian Machine Learning for Quantifying Uncertainty in Surrogate Modelling
Archie Luxton
14th September 2022 09:00

## Slide 2: Background : Project Aims
Typically Finite Element (FE) models
Ensures a structure will be safe
Predicts the response to earthquakes, wind loading…
Acts as a record of design
E.g. Oasys GSA
A nice picture?

## Slide 3: Background : Project Objective
Develop uncertainty-aware Neural Network-based surrogate models that can predict the modal frequencies of 3D structures and communicate the uncertainty in those predictions.

## Slide 4: Background : Modal Analysis
Modal analysis predicts the resonant frequencies of structures
Modal frequencies of a structure shouldn't match frequency of:
  Earthquakes
  Footsteps and sway
  Wind flutter
Millennium Bridge, London
Mexico City earthquake, 1985
Broughton Bridge collapse, 1826

## Slide 5: Background : Modal Analysis Using GSA
Oasys GSA can perform modal analysis
Calculates many modal frequencies of a structure
Solves a generalised eigenvalue problem
Define geometry
Define simulation parameters
Wait between 3s – 18mins

## Slide 6: Background : Advantages / Disadvantages of GSA Analysis
GSA Modal Analysis
Accurate
Explainable
Expensive
Complexity scales with size of structure
Platform-specific
Automation requires APIs/SDKs
Specific to one problem

## Slide 7: Background : Neural Network Surrogate Models
Trained on FE simulation results
Approximates full FE simulations
Faster inference
Not specific to one problem

## Slide 8: Background : Surrogate vs GSA Analysis
GSA Modal Analysis | Modal Analysis via NN-based surrogate
Accurate | Is an approximation
Explainable | Hard to explain
Expensive | Cheap predictions
Complexity scales with size of structure | Complexity constant w.r.t. size of structure
Platform-specific | Platform agnostic / portable
Automation requires APIs/SDKs | Automation very straightforward
Specific to one problem | Applicable to many problems

## Slide 9: Methodology : Overview
Research types of Uncertainty Quantification (UQ)
Implement and compare UQ methods on simple NNs
Train uncertainty-aware, NN-based surrogates
Analyse uncertainty
  In domain vs. OOD
  Re-training
  Visualisation & communication

## Slide 10: Methodology : Methods to Add Uncertainty Quantification to NNs
Two stochastic methods investigated:
  MC Dropout (Gal and Ghahramani, 2016)
  Stochastic Gradient Langevin Dynamics (SGLD) (Welling et al., 2011)
Both methods apply stochasticity. Sampling stochastic outputs => approximation to predictive posterior distribution

## Slide 11: Methodology : MC Dropout
inputs
hidden layer(s)
output layer(s)
epoch
loss
TRAINING
Learning weights + stochastic dropout
INFERENCE
Using learned weights + stochastic dropout
approximation to predictive posterior

## Slide 12: Methodology : Stochastic Gradient Langevin Dynamics (SGLD)
inputs
hidden layer(s)
output layer(s)
inputs
hidden layer(s)
output layer(s)
epoch
loss
TRAINING
burn-in
period
save model weights at checkpoints
Gaussian noise
η ~ N(0, lr)
frequency (Hz)
density
INFERENCE
approximation to predictive posterior

## Slide 13: Results : Comparison of Models
 |  | MC Dropout | SGLD
Training time |  | 71s | 230s
Average RMSE: | Training | 0.007 | 0.000
 | Validation | 0.008 | 0.005
 | Test | 2.034 | 1.983
Average CI Width (+/- 1σ) | Training | 0.055 | 0.033
 | Validation | 0.057 | 0.035
 | Test | 0.273 | 0.175

## Slide 14: Results : Surrogate Model Demo – GH/Rhino with RESTful API

## Slide 15: Results : Speed
Chart: GSA Analysis
| 1 | 8 | 125 | 343 | 1000 | 1728 | 3375 | 4913 | 8000 | 10648 | 15625 | 19683 | 27000
 | 3.65 | 5.842 | 14.954 | 18.925 | 36.2857 | 61.9 | 117.3333 | 157.5 | 281 | 371.9 | 618.9 | 946.1 | 1069
Chart: NN-based Surrogate
| 1 | 8 | 125 | 343 | 1000 | 1728 | 3375 | 4913 | 8000 | 10648 | 15625 | 19683 | 27000
 | 0.038209 | 0.03943 | 0.035761 | 0.040377 | 0.038767 | 0.032799 | 0.031372 | 0.035121 | 0.036586 | 0.034084 | 0.032739 | 0.036979 | 0.035499
5x5x5:
500x speedup
30x30x30:
28,000x speedup
22x22x22:
11,000x speedup

## Slide 16: Results : Accuracy and Uncertainty: Reference Datasets

## Slide 17: Results : Uncertainty - Unseen Geometries

## Slide 18: Results : Retraining with Additional Data

## Slide 19: Results : Uncertainty - Unseen Geometries

## Slide 20: Methodology Applying UQ to NNs - MC Dropout
num_x
num_y
num_z
dim_x
dim_y
dim_z
During training
Making prediction
Dropout as SRT

## Slide 21: Methodology : MC Dropout
num_x
num_y
num_z
dim_x
dim_y
dim_z
TRAINING
num_x
num_y
num_z
dim_x
dim_y
dim_z
INFERENCE